## Slide 1: S-RED
Md. Zarif Ul Alam
1705010

## Slide 2: Reference
T. J. Ott, T. V. Lakshman and L. H. Wong, "SRED: stabilized RED," IEEE INFOCOM '99.

## Slide 3: Overview
SRED : Stabilized Random Early Drop
Pre-emptively discards packets with a load-dependent probability when a buffer in a router in the Internet or an Intranet seem congested
Additional Feature from RED : Wide range of load levels help it stabilize its buffer occupation at a level independent of the number of active connections
Presents a mechanism for statistically estimating the number of active flows in a bottleneck link

## Slide 4: Methodology
Zombie List : M recently seen flows, with extra information “count” and “time stamp”
Zombies : flows in the zombie list
Zombie list starts out empty, As packets arrive, as long as the list is not full, for every arriving packet the packet flow identifier (source address, destination address, etc.) is added to the list, the count of that zombie is set to zero, and its timestamp is set to the arrival time of the packet

## Slide 5: Methodology
Once the zombie list is full it works as follows: Whenever a packet arrives, it is compared with a randomly chosen zombie in the zombie list.
  Hit : If the arriving packet’s flow matches the zombie we declare a “hit”.
    Count ++
    Update timestamp
  No Hit : If the two are not of the same flow, we declare a “no hit”. In that case, with probability p the flow identifier of the packet is overwritten. With probability 1 - p there is no change to the zombie list.

## Slide 6: Usefulness
The number of active flows can be estimated from the average hit rate
This method does not require keeping per-flow state
Buffer occupancy can be controlled to hover around a preset value which is independent of the number of active connections
Using hit mechanisms to identify misbehaving flows as misbehaving sources are likely to get higher numbers of hits since they send more packets

## Slide 7
THANK YOU